## Slide 1: INTERNSHIP
Week 3 Review
By Kaluva Chandrashekar
25MTRVE005
3rd Sem
Jain University

## Slide 2: Day 1 – KiCad Schematic Review & Connection Verification
AXP2101 Schematic: Reviewed the AXP2101 pin-level connections and surrounding power circuitry.
ESP32-S3 Schematic: Reviewed the ESP32-S3 pins and required circuit connections.
J2 13-Pin Connector: Connected and reviewed the required signals of the J2 connector step by step.
SPI Flash Interface: Reviewed the ESP32-S3 SPI Flash signals and their connections.
USB & Clock Circuit: Verified USB D−/D+ connections, resistors, crystal, and associated capacitors.
CHIP_PU & Power Connections: Reviewed the reset/pull-up circuit along with +3V3 and GND connections.
Combined Schematic Verification: Checked the AXP2101 and ESP32-S3 sections together; remaining connectivity verification and ERC/DRC checking are in progress.

## Slide 3: DAY 2 – FPGA Basics & Verilog Implementation
Reviewed FPGA architecture and programmable logic resources.
Worked with the Gowin GW1NSR-4C FPGA used on the T-FPGA board.
Created a Gowin FPGA project using Gowin EDA V1.9.12.03.
Selected device: GW1NSR-LV4CQN48PC6/I5.
Created a basic Verilog design for FPGA output testing.
Configured FPGA I/O pin assignments using the Floor Planner.
Generated the FPGA bitstream and programmed the board using the Gowin USB Cable.
Verified the FPGA hardware output on the T-FPGA board.

## Slide 4: DAY 3 – PLL & Frequency Detection
Studied practical clock generation and frequency-detection implementation.
Worked with the Gowin IP Core Generator.
Generated the PLLVR IP for the GW1NSR-4C FPGA.
Configured the PLL with 27 MHz input clock and 54 MHz output clock.
Integrated the generated PLL module into the Verilog design.
Completed synthesis, Place & Route and bitstream generation.
Programmed the FPGA and verified the implemented design on hardware.

## Slide 5: DAY 4 – Cortex-M3 & FPGA Communication
Worked with the embedded Cortex-M3 processor in the GW1NSR-4C EMPU.
Installed and used Gowin MCU Designer (GMD) and the Gowin EMPU reference software.
Imported and built the cm3_demo reference project.
Enabled the AHB2 Master demonstration in the software project.
Developed Cortex-M3 firmware to access the FPGA register space at 0xA0000000.
Built the firmware successfully with 0 errors and 0 warnings.
Generated cm3_demo.bin and programmed it together with the FPGA bitstream.
Integrated AHB2 Master signals with FPGA-side register logic and verified the programmed hardware.

## Slide 6: DAY 5 – ESP32-S3 Wi-Fi & T-FPGA Web Interface
Configured the ESP32-S3 using Arduino IDE 2.3.10.
Selected ESP32S3 Dev Module and uploaded the Wi-Fi/web-server program.
Configured the ESP32-S3 as a Wi-Fi Access Point named TFPGA_DAY4.
Implemented a web server to display T-FPGA status in a browser.
Connected FPGA communication data lines to ESP32-S3 GPIO inputs.
Displayed D0, D1, D2, D3 and the combined FPGA value on the webpage.
Built the Cortex-M3 firmware and enabled AHB2 Master in the FPGA EMPU configuration.
Completed FPGA synthesis, Place & Route and programming using Gowin Programmer.
Final browser verification showed the communication fields, with further non-zero data-transfer verification remaining.

## Slide 7: WEEK 3 – Overall Progress
Completed practical FPGA development and programming using Gowin EDA.
Implemented and tested a PLL-based clock-generation stage.
Worked with the GW1NSR-4C embedded Cortex-M3 and AHB2 Master interface.
Built Cortex-M3 firmware using Gowin MCU Designer.
Integrated FPGA-side register logic with the Cortex-M3 AHB2 interface.
Configured ESP32-S3 Wi-Fi and implemented a browser-based T-FPGA status interface.
Established the ESP32-S3 FPGA communication GPIO path.
Completed the main Week 3 implementation stages and identified the remaining communication verification work.

## Slide 8
THANK YOU